## Slide 1
implementation deck
Dense-grid GPU narrow phase for surgical collision
The current plugin removes object-AABB broad-phase latency, generates primitive tissue/blade pairs on the GPU, deduplicates them, and runs exact triangle contact tests device-side.
234k tris
largest benchmark
2.12M
unique pairs
23.90 ms
GPU compute
Current execution shape
SOFA pair
tissue + blade only
v
Dense grid
one cell space, two id lists
v
Exact contact
1 thread per unique pair
Detection-only output keeps contacts on device; CPU sees counters and timings.
SofaGpuCollision | WSL/CUDA surgical simulation path

## Slide 2
GPU SURGICAL COLLISION
Default SOFA frame flow
SOFA normally advances a simulation by traversing the scene graph, solving mechanics, detecting contacts, then applying collision response before the next visual update.
1. Scene state
MechanicalObject positions, velocities, topology, mappings
->
2. Forces
mass, damping, FEM force fields, constraints
->
3. Integrate + solve
ODE solver assembles/apply system; linear solver updates state
4. Collision detection
broad phase -> narrow phase -> contact candidates
->
5. Collision response
contact manager builds response constraints or penalty forces
->
6. Update outputs
mapped collision/render geometry, logging, visualization
Data model
The default component path is CPU-friendly: scene graph objects own data, algorithms read/write through SOFA containers, and mappings synchronize derived geometry.
Collision pipeline
Broad phase decides which models may interact; narrow phase tests primitives and emits contacts; response consumes those contacts.
Response is last
That matches your architecture: keep detection, metadata, and solve on GPU first; move final collision response after the device pipeline is stable.
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 3
GPU SURGICAL COLLISION
Why the default CPU path limits surgical GPU simulation
The issue is not only raw CPU speed. The larger limitation is ownership: if the CPU owns state, every GPU stage becomes a temporary accelerator instead of the main simulation path.
CPU-owned default path
Scene graph traversal
component calls and Data access happen frame-by-frame
Mechanical solve on CPU
force assembly, constraints, and sparse/direct solves can dominate
Collision on CPU
broad/narrow/contact generation stay host-side in standard path
Two-object surgery problem
object AABB broad phase adds little when tissue and blade always interact
->
move
ownership
to GPU
GPU-resident target
Tissue + tool state
positions, velocities, FEM element data, constraints in VRAM
Dense-grid primitive filtering
skip redundant object AABB culling; generate tissue/blade pairs on device
Exact contacts + metadata
deduplicated candidate pairs feed device contact buffers
GPU solve then response
linear solve and response consume contacts without CPU round-trip
Design rule
A fast CUDA kernel is not enough. The win comes when geometry, candidates, contacts, solver vectors, and response data stop leaving VRAM each step.
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 4
GPU SURGICAL COLLISION
Total execution flow now
Broad phase is no longer doing object AABB rejection for this benchmark path. It is a pair emitter; primitive filtering is inside the GPU dense-grid narrow phase.
CPU / SOFA orchestration
GPU / CUDA narrow phase
CollisionPipeline
calls broad and narrow phases
GpuCollisionBroadPhase
useObjectAabbCulling=false; emits tissue/blade pair
GpuCollisionNarrowPhase
extracts SOFA triangles and builds host DeviceTriangle arrays
H2D upload
40 bytes per triangle, every measured step today
->
H2D
boundary
large path:
3.18 MB / step
Dense grid buckets
insert tissue ids and blade ids per cell
Candidate generation
per cell cross product: tissueCount * toolCount
Sort + unique
removes duplicate pairs from multi-cell triangles
Exact contacts
SAT triangle test; contact buffer stays GPU-side
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 5
GPU SURGICAL COLLISION
Dense spatial grid: one grid, two per-cell lists
The scene is divided once. Each cell stores tissue triangle ids and blade triangle ids separately, then generates candidate pairs from the cross-product inside that cell.
1. Triangle AABB overlaps cells
T
T
B
T
B
T
T = tissue
B = blade
2. A cell owns two id arrays
cellId = x + y*nx + z*nx*ny
cellTissueIds[cellId][0..x-1]
cellToolIds[cellId][0..y-1]
Counts are filled with atomicAdd during triangle insertion.
This is not two scene grids. It is one scene grid with two primitive lists per cell.
3. Candidate pairs are local
pairsInCell = x * y
T17
T18
T42
B3
B4
3 tissue ids x 2 blade ids = 6 raw pairs
Duplicates are removed before exact testing because large triangles may touch multiple cells.
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 6
GPU SURGICAL COLLISION
CUDA kernels and thread allocation
The current GPU narrow phase is a fixed sequence of reusable kernels plus a Thrust dedup pass before exact contact generation.
Stage
Thread mapping
Output
clear grid
1 thread = 1 cell
zero cell counts and counters
compute AABBs
1 thread = 1 triangle
inflated tissue/blade bounds
insert triangles
1 thread = 1 triangle
cell id lists via atomicAdd
generate pairs
1 block = 1 cell
encoded uint64 raw pairs
thrust::sort + thrust::unique
device-wide parallel primitives
unique candidate pairs
exact contact
1 thread = 1 unique pair
DeviceExactContact buffer
Exact contact kernel
decode ids; load DeviceTriangle A/B
run triangle SAT overlap test
if hit: atomicAdd(contactCount)
Why dedup is active
A triangle can overlap many cells. Without sort/unique, exact testing repeats pairs.
Current benchmark uses deduplicatePairs=true.
Main call path
GpuCollisionNarrowPhase::endNarrowPhase()
-> computeDenseGridTriangleContacts()
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 7
GPU SURGICAL COLLISION
Memory layout and transfer model
Device memory is allocated once and reused. The biggest remaining cost is that the current path still repacks and uploads triangle geometry every step.
Global VRAM workspace
Buffer
Purpose
DeviceTriangle[]
tissue and blade triangle records
DeviceAabb[]
inflated per-triangle bounds
DeviceCellBucket[]
per-cell tissue/tool counts
cellTissueIds / cellToolIds
flat primitive id lists
uint64 candidatePairs[]
encoded tissueId/bladeId pairs
DeviceExactContact[]
GPU contact output
Transfer boundary today
H2D every step
(tissueTris + bladeTris) * 40 bytes
Large scene: 3.18 MB per step
D2H minimized
Contacts stay device-side; only counters are copied back.
Measured D2H: 16 bytes/step
Implication
GPU compute is not the full story. Extraction, packing, H2D upload, syncs, and SOFA traversal still sit in wall time.
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 8
GPU SURGICAL COLLISION
Benchmark scaling: wall time vs GPU compute
The GPU kernels scale into the CPU range at the largest scene, but total GPU wall time remains dominated by transfer and orchestration overhead.
CPU wall
GPU compute
GPU wall
medium
38k
CPU wall
4.96 ms
GPU compute
3.38 ms
GPU wall
8.22 ms
large
80k
CPU wall
8.05 ms
GPU compute
4.00 ms
GPU wall
11.76 ms
xlarge
146k
CPU wall
10.59 ms
GPU compute
10.67 ms
GPU wall
42.43 ms
xxlarge
234k
CPU wall
24.75 ms
GPU compute
23.90 ms
GPU wall
71.25 ms
Bar length is normalized to the slowest measured GPU wall time: 71.25 ms.
Case
Tris
CPU
GPU compute
medium
38k
4.96 ms
3.38 ms
large
80k
8.05 ms
4.00 ms
xlarge
146k
10.59 ms
10.67 ms
xxlarge
234k
24.75 ms
23.90 ms
Largest scene
234k tris
CPU wall: 24.75 ms
GPU compute: 23.90 ms
GPU wall: 71.25 ms
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.

## Slide 9
GPU SURGICAL COLLISION
Why CPU still wins in full wall time
The implementation is doing the right GPU-side work. The benchmark exposes what remains outside the GPU-resident architecture.
GPU wall minus compute
medium
4.84 ms
large
7.76 ms
xlarge
31.76 ms
xxlarge
47.35 ms
This gap includes extraction, packing, H2D transfer, synchronization, SOFA traversal, and batch overhead.
What is already good
Object broad phase removed. Grid filtering, dedup, exact contacts, and contact residency are active.
No overflows; 2.12M unique pairs at xxlarge.
What blocks speedup
1. Per-step triangle upload scales with geometry.
2. Dense grid launches over many empty cells.
3. Sort/unique grows with duplicate candidates.
4. GTX 1650 Ti launch/sync overhead is visible.
Next implementation step
Keep geometry resident, build active-cell lists, use CUB compaction, then connect GPU response so contacts never return to CPU.
Source: current SofaGpuCollision implementation and benchmark reports, generated 2026-05-08.